## Slide 1
OPENING PROMISE
The PDU protocol is the contract that lets software safely touch power.
Current framed protocol, test plan, and future mission-ready direction.
Teensy
low-level owner
PDU MCU
power + safety
Rails
SOH
PDU protocol | 01
Notes: Open by framing the protocol as a safety boundary. The point is not just data exchange; it is the contract that allows software to command power hardware without accidental toggles.

## Slide 2
WHY CHANGE IT
One corrupted byte should not be able to become a power command.
Old style
newline + ad hoc fields
no CRC
weak recovery
Current style
framed packet
sequence ACK
CRC checked
fragile stream
recoverable transaction
PDU protocol | 02
Notes: Explain why robustness matters before explaining how it works. The old path could not reliably distinguish a clean command from a damaged stream. The new path makes each command a checked transaction.

## Slide 3
CURRENT PROTOCOL
A frame gives every UART message a beginning, a size, and a checksum.
SOF
0xA5
VERSION
0x02
TYPE
request
OPCODE
what to do
SEQ
match reply
STATUS
result
LEN
bytes
PAYLOAD
data
CRC
detect error
SOF finds the frame. LEN bounds it. CRC decides whether it is trusted.
PDU protocol | 03
Notes: Walk left to right. SOF is start of frame. Length prevents guessing how many bytes to read. CRC rejects corrupted frames before any hardware is touched.

## Slide 4
CORE MECHANISM
Every command is a request, validation step, hardware action, and measured response.
Host sends
request
PDU checks
length + params + CRC
Touch
hardware
Reply
state
before
No hardware change happens until the packet is structurally valid.
PDU protocol | 04
Notes: This is the safety story in one slide. The parser rejects noise. The handler rejects bad length and invalid output IDs. Only then does the firmware touch pins.

## Slide 5
CURRENT API
The current API is intentionally small.
0x01
GET
PROTOCOL_INFO
0x02
GET
SUMMARY_STATUS
0x03
GET
RESET_INFO
0x10
GET
OUTPUT_STATE
0x11
SET
OUTPUT_STATE
Small APIs are easier to test, easier to explain, and harder to misuse.
PDU protocol | 05
Notes: Avoid apologizing for small scope. The whole point is a stable protocol core. We can add more opcodes later without weakening the transport.

## Slide 6
ABSTRACTION
The protocol exposes logical outputs, not raw pins.
Host says
PDU_OUTPUT_12V = ON
PDU decides
SW_5V_EN4
+
SW_12V_EN1
Telemetry says
12V logical state
PDU protocol | 06
Notes: Use 12V as the example. The host should not need to know that the 12V rail depends on another 5V enable. That kind of sequencing belongs inside the PDU.

## Slide 7
SOH TELEMETRY
One summary packet gives the demo a credible health story.
output
bitmap
reset
cause
fault
bitmap
uptime
seconds
capability
bits
GET_SUMMARY_STATUS
This is the packet that feeds judge-visible SOH without overbuilding EPS services.
PDU protocol | 07
Notes: Explain that SOH does not need every sensor on day one. It needs a compact packet that proves the PDU is alive, outputs are known, and reset history is visible.

## Slide 8
TEST WHY
We test the protocol because the parser is part of the safety system.
bad CRC
ignored
bad length
BAD_LENGTH
bad ID
BAD_PARAM
bad opcode
BAD_OPCODE
good command
state reply
The test question is simple: can malformed input ever touch hardware?
PDU protocol | 08
Notes: This is the main test philosophy. The safest parser is not the one that handles happy paths; it is the one that reliably refuses malformed data.

## Slide 9
TEST PLAN
Testing should climb from pure bytes to real rails.
1. parser byte tests
2. handler contract tests
3. bench UART tests
4. FlatSat rail readback
PDU protocol | 09
Notes: Recommend starting with tests that do not require hardware: build frames, corrupt frames, verify responses. Then use bench UART, then FlatSat current/rail readback.

## Slide 10
TEST EXAMPLES
The first host-side tests should be boring and repeatable.
Build frame
flip one CRC byte
expect silence
Send SET_OUTPUT
read back state
verify seq echo
Power cycle PDU
GET_RESET_INFO
show SOH
PDU protocol | 10
Notes: These are the practical tests a controller-side repo can automate quickly. They establish framing, command acknowledgement, and health visibility.

## Slide 11
FUTURE PROTOCOL
The future protocol should keep the frame and generalize the objects.
same frame
objects
outputs
sensors
faults
supervisors
capabilities say
what exists
Do not break the transport to add missions. Add discoverable objects above it.
PDU protocol | 11
Notes: Answer the generic-enough question. The frame is generic. The current payload model is PDU-specific. Future missions should add an object model and capabilities without changing the base frame.

## Slide 12
FUTURE TELEMETRY
Future SOH should add richer telemetry without making commands unsafe.
outputs
enable + sensed state
sensors
voltage + current + temp
faults
latched + active bits
events
boot + fault + state change
The rule stays the same: commands request intent; the PDU owns safety decisions.
PDU protocol | 12
Notes: This is the future direction slide. More telemetry is useful, but it should not push unsafe low-level pin choreography up into the host.

## Slide 13
ROADMAP
Freeze the base frame, then add capability-discovered features.
now
outputs + summary
next
faults + events
later
chargers + Pi supervisor
stable transport, evolving payloads
PDU protocol | 13
Notes: Make the migration plan explicit. We are not trying to finish every future mission feature now. We are freezing the reliable base and adding discoverable extensions.

## Slide 14
CLOSING LINE
The win is not a bigger protocol. The win is a protocol we can trust.
Current: robust output control + SOH. Future: discoverable EPS objects on the same safe frame.
test
observe
ack
reject
evolve
PDU protocol | 14
Notes: Close with the principle. Trust comes from bounded frames, CRC, explicit status, sequence ACK, and a scope that students can test.