## Slide 1
The current PDU architecture is simple, but too tightly coupled.
Current behavior first. Then the recommended refactor.
221\n
2 = SetSwitch
2 = SW_3V3_1
1 = ON
One small UART command drives real power hardware.
That is useful for demos, but it needs stronger boundaries before students treat it as plug-and-play mission infrastructure.
PDU architecture | 1
Notes: Open with the direct summary: this works, but it is currently a demo-style architecture. The key issue is not UART; it is the lack of clean layers between command intent and GPIO behavior.

## Slide 2
Today, the PDU speaks ASCII-offset bytes over UART.
It is not a readable command sentence. It is a tiny numeric protocol encoded as characters.
BYTE 1
Command byte
ASCII character minus 48 becomes the packet type.
BYTE 2
Switch byte
ASCII character minus 48 selects the rail or device.
BYTE 3
State byte
ASCII character minus 48 becomes off or on.
END
Newline
CR or LF ends the command frame.
'2' - 48 = 2 '1' - 48 = 1
PDU architecture | 2
Notes: Explain the current wire format plainly. Students can understand it quickly, but it is easy to confuse with either text commands or real binary framing.

## Slide 3
The active firmware path is one straight line.
This is why it is easy to demo and easy to outgrow.
1
FreeRTOS task
2
UART poll
3
Decode packet
4
Switch GPIO
5
Send reply
The same handler currently mixes protocol parsing, command dispatch, physical GPIO behavior, and telemetry packing.
PDU architecture | 3
Notes: Keep this slide fast. The path is not complicated. The architectural problem is that too many responsibilities live in the same place.

## Slide 4
This is fine for learning the board, not for mission reuse.
The current design teaches the hardware path, but not a durable subsystem boundary.
CURRENT STRENGTH
Good today
Fast to test
Easy to inspect on serial
Small enough for a demo
Direct proof of GPIO behavior
CURRENT RISK
Hard tomorrow
Raw struct assumptions
No version or CRC
Weak error model
Physical rails leak upward
MENTAL LOAD
Student problem
They must reason about UART, enums, GPIO pins, composite rails, and telemetry layout at the same time.
PDU architecture | 4
Notes: Make the student angle explicit. The system is understandable, but it makes students hold too many layers in their head at once.

## Slide 5
Option 2 gives the PDU a real EPS interface.
The wire protocol should describe mission intent, not GPIO trivia.
LAYER 1
Pi / F Prime
Mission commands and telemetry.
LAYER 2
Teensy 4.1
EPS client and supervisor.
LAYER 3
PDU ICD
Versioned UART contract.
LAYER 4
PDU MCU
GPIO and sensing owner.
magic | version | type | seq | len | payload | crc
PDU architecture | 5
Notes: Avoid overexplaining. This is the recommended shape: Pi speaks mission behavior, Teensy supervises, PDU owns hardware details.

## Slide 6
The new commands should sound like EPS behavior.
Students should think in rails, health, faults, and safety actions.
PING
Prove the link is alive.
GET_CAPS
Report what this board supports.
SET_RAIL
Turn a named rail on or off.
GET_SOH
Return compact health state.
PULSE_RESET
Reset a supervised device.
GET_FAULTS
Report latched fault flags.
PDU architecture | 6
Notes: This slide is the heart of the recommendation. The API should match the spacecraft behavior students are trying to control.

## Slide 7
The PDU firmware becomes four small modules.
Each module has one job, so students know where to look.
MODULE
Transport
Read a frame.
Check CRC.
Return bytes.
MODULE
Protocol
Decode message type.
Validate payload.
Encode reply.
MODULE
EPS logic
Apply rules.
Reject unsafe state.
Build SOH.
MODULE
Board driver
Own pins.
Read sensors.
Hide hardware quirks.
No mission software should need to know that SW_12V also needs SW_5V_EN4.
PDU architecture | 7
Notes: Say the practical win: composite rail behavior stays inside the board driver. Higher layers request intent.

## Slide 8
The student reasoning path gets much cleaner.
Every layer answers a different question.
QUESTION 1
Mission layer
What do we want the spacecraft to do?
Example: turn payload power on.
QUESTION 2
Protocol layer
Was the request valid, versioned, acknowledged, and checked?
Example: SET_RAIL accepted.
QUESTION 3
Hardware layer
Which pins and sensors prove the rail actually changed?
Example: rail state and faults reported.
PDU architecture | 8
Notes: This is the teaching value. Students can debug one layer at a time instead of mixing mission intent, packet bytes, and GPIO effects.

## Slide 9
Recommendation: refactor to Option 2 first.
Keep it small. Make the boundary real. Do not jump straight to a generator yet.
START
Step 1
Freeze the existing ASCII protocol as legacy v1.
Document examples and known limits.
BUILD
Step 2
Add a v2 framed EPS ICD.
Implement PING, GET_CAPS, SET_RAIL, GET_SOH.
INTEGRATE
Step 3
Write the Teensy client library.
Then connect F Prime through EpsService/EpsAdapter.
Best outcome: students reason through mission commands, protocol frames, and hardware proof separately.
PDU architecture | 9
Notes: Close with the concrete recommendation. Option 2 is enough structure for future missions without making the first refactor too large.